## Slide 1
Precision irrigation for one Egyptian feddan
24 autonomous zones · LoRa edge control · crop-aware decisions
Deliver the right amount of water
to the right zone at the right time.
24
ZONES
Prototype system
for field validation
Notes: [Sources]
Project architecture and costs supplied by user.

## Slide 2
The farm challenge is uneven demand
A single schedule cannot reflect crop, soil, or growth-stage variability
24 zones can have different crops and soil behavior.
Over-irrigation can increase water and nutrient losses.
Manual decisions rarely include continuous local feedback.
Design response
Sense → decide → deliver → verify
Notes: [Sources]
Project brief; FAO Crop evapotranspiration framework.

## Slide 3
One resilient control loop per zone
Sensors are wired locally; LoRa connects each ESP32 to the Raspberry Pi
Capacitive moisture + SHT31 + Hall flow sensor.
ESP32 controls a protected driver—not the valve directly.
SX1278 LoRa carries telemetry, commands and acknowledgements.
ESP32 → LoRa → Raspberry Pi
← crop model + SQLite ←
Notes: [Sources]
Project hardware architecture supplied by user.

## Slide 4
The gateway makes decisions; the node enforces safety
Raspberry Pi selects the configured crop model once per zone.
It calculates a target volume and sends an irrigate command.
ESP32 closes locally at target, no-flow, high-flow or time limit.
Safety remains local
even if communications fail.
Notes: [Sources]
Project safety design supplied by user.

## Slide 5
Five crop models reflect different water-demand patterns
Tomato · potato · cucumber · pepper · onion
Each model is trained only on its own crop dataset.
Growth stage and soil type are stored as context, not fabricated sensors.
Model outputs an irrigation decision; the water layer sets volume.
Tomato Potato
Cucumber Pepper Onion
Notes: [Sources]
FAO crop-factor table: https://www.fao.org/4/s2022e/s2022e07.htm

## Slide 6
Synthetic data are research-informed—not field proof
Transparent assumptions make the prototype testable and replaceable
Kc stage patterns guide demand simulation: ETc = Kc × ETo.
Soil retention changes depletion behavior for sandy, loamy and clay soil.
Noise is bounded; no independent random feature columns.
Required next step:
calibrate with Egyptian field data.
Notes: [Sources]
FAO Crop water needs https://www.fao.org/4/s2022e/s2022e07.htm; FAO-56 https://www.fao.org/4/x0490e/x0490e00.htm

## Slide 7
The ML pipeline is reproducible and edge-ready
12,000 synthetic records per crop; fixed seed.
70% train · 15% validation · 15% held-out test.
Compares logistic regression, random forest and gradient boosting by validation F1.
model.joblib + metadata
loaded once at gateway start
Notes: [Sources]
Project ML implementation.

## Slide 8
Flow feedback turns commands into verified delivery
Interrupt pulse count ÷ calibrated pulses/litre = total litres.
Flow rate is calculated over a timed interval.
Actual delivery closes the event loop in SQLite and Telegram.
Target 20 L
→ valve closed at 20 L
Notes: [Sources]
Project firmware design supplied by user.

## Slide 9
The platform produces operational evidence
SQLite data supports traceability and weekly action
Sensor readings: moisture, temperature, humidity and flow.
Irrigation events: target, actual delivery, status and crop.
Weekly reports: water by zone/crop, failures and average conditions.
Telemetry → model → command
→ delivery → report
Notes: [Sources]
Project database/reporting design supplied by user.

## Slide 10
Hardware cost: ≈ 66,000 EGP
One feddan / 24 zones · existing main pump excluded
24 zones
58,776 EGP
Central edge
≈ 7,500 EGP
TOTAL
≈ 66,300 EGP
Includes ESP32, SX1278, sensors, valves, drivers, boxes, sprinklers, Raspberry Pi, LoRa, storage, PSU, fittings and basic filter/pressure components.
Notes: [Sources]
Cost schedule supplied by user. Main pump expressly excluded.

## Slide 11
The cost schedule is transparent
Per-zone hardware × 24 = 58,776 EGP
ESP32 + SX1278: 14,784 EGP
Sensors (moisture, SHT31, Hall): 10,320 EGP
Valves, driver/protection, enclosure/wiring, sprinkler: 33,672 EGP
2,449 EGP
per zone
Notes: [Sources]
Cost schedule supplied by user.

## Slide 12
Value comes from precision, not a guaranteed percentage
Use water and energy economics that match each farm
Potentially 30–60% less irrigation water depends on baseline method, crop, soil and management.
Each zone receives its own sensing and decision path.
More precise timing/volume can reduce the risk of over-irrigation and leaching.
Notes: [Sources]
FAO integrated soil management manual https://www.fao.org/4/x4799e/x4799e.pdf; outcome figures are conditional, not a deployment guarantee.

## Slide 13
ROI should use the farm’s real pumping cost
Avoid inventing a universal water price
1,000 m³ baseline
× 40% reduction
= 400 m³ saved
Money saved = 400 × X EGP
X = actual pumping cost per m³
Next: field pilot, calibrate sensors, capture baseline water/energy, validate the models.
Notes: [Sources]
Savings example and economic framing supplied by user.